## Slide 1: CMP-COMPARE INSTRUCTION
CMP works like sub instruction with the only difference that it doesn’t change operands.
Subtracts source operand from destination operand and updates flags only.
Example
CMP AX, BX ;
Performs (AX-BX) and updates flags. Source and destination values remain unchanged.

## Slide 2: CMP INSTRUCTION-Effect on FLAGS
MOV AX, 5
CMP AX, 5; Which flag will be set?
Zero flag will be set, ZF=1, also PF=1;
MOV AX, 5
MOV CX, 10
CMP AX, CX; Which flag will be set?
Subtracting 10 from 5 requires borrow, so carry flag will be set, CF=1; SF=1;

## Slide 3: CMP INSTRUCTION-Effect on FLAGS
MOV DL, 15
MOV BL, 4
CMP DL, BL; Which flag will be set?
None
MOV AL, 127
MOV BL, -2
cmp AL, BL; Which flag will be set?
Subtracting -2 from 127 makes it 129, max positive number in one byte is 127? So overflow occurs. OF=1; SF=1 (negative result)

## Slide 4: CMP AND JUMP INSTRUCTIONS
A compare instruction (CMP) without jump instruction is meaningless. Why?
There is no use of comparison if you’re not taking a decision after comparison.
In a jump instruction, decision is taken based on flag bits.
Those flag bits might have been updated previously by an ALU instruction or a CMP instruction.
Decisions are taken using conditional jump instructions.

## Slide 5: JUMP INSTRUCTIONS
What are jump instructions?
  Program control transfer instructions used to control flow of execution in a program.
Why do we need jump instructions?
  To do a task repeatedly?
  To take a decision based on a result?
  To switch between options based on some requirement?

## Slide 6: Labels
Labels can be defined by a label name terminated with a colon.
For example, to declare a label named start you can write start:
To declare a label named repeat you can write repeat:
Each label in a program has its own unique address.
Labels can be used as reference addresses in program execution.

## Slide 7: JUMP INSTRUCTIONS
Jump instructions can be used to start executing instructions from any address location within memory.
Two main types of jump instructions
Unconditional jump-
  To start executing instructions from an address unconditionally.
Conditional jump
  To start executing instructions from an address based on some condition.

## Slide 8: UNCONDITIONAL JMP INSTRUCTION
JMP 3;
Starts executing instructions from physical address formed via segment offset pair CS:0003.
JMP begin;
Starts executing instructions from address specified by label “begin”.
Each label in a code is associated with a unique address in memory.

## Slide 9: CS and IP register-overview
Instructions are placed in code segment and variables are stored in data segment.
Code segment register (CS) contains the starting address of code segment.
Instruction pointer register (IP) holds the address of next instruction to be executed. Points in the code segment.
When you write JMP 3h, the value 3h is assigned to IP and processor starts executing instructions from physical address formed using CS:IP pair.
For example, if CS=0100hex and IP is assigned IP=0003; Physical address would be
CS=01000; shifted left by one hex digit
IP =00003;
Physical address=01003

## Slide 10: JMP instruction-CS and IP register
MOV BX, 64h
ADD AX, BX
JMP 3;
When third instruction executes, IP is updated to IP=0003 and processor starts executing instructions from physical memory address 01003
CS=01000;
IP =00003;
Physical address =01003

## Slide 11: UNCONDITIONAL JMP-Example
    JMP start ; unconditional JMP instruction
    VAR1 DB 5
    VAR2 DW 77
    start: ; start: is a label/address in a program
    MOV AX, 2;
    ADD AX, 1;
    .EXIT
  Used JMP START at the beginning to skip executing “variable declaration statements” as executable instructions.

## Slide 12: Conditional JUMP instructions
In a conditional jump instruction, two parts are specified
Combination of characters to specify which flags bits will be checked?
An address from which instructions will be executed if condition comes out to be true.
Example
JC Lab1; Read as Jump if carry;
Processor starts executing instructions from label “Lab1” if carry flag CF=1.

## Slide 13: Example- Number is even/odd?
Task: If number N1 is even put 0 in AL else put FF in AL?
  MOV AL, [N1]
  SHR AL,1 ; Shifts right AL by one bit, CF becomes 1;
  JC L1 ; Jump to label L1if CF=1 (odd number)
  MOV AL, 0 ;
  JMP L2 ;skip executing instructions specified at L1
  L1:
  MOV AL, 0xFF
  L2:
  MOV AX,0x4C00
  INT 21H
  N1 db 7;

## Slide 14: Other Conditional JUMP instructions
JC ;Jump if carry flag set
JNC ;Jump if not carry
JZ ;Jump if zero flag set
JNZ ;Jump if zero flag not set
JE ;Jump if zero flag set
JNE ;Jump if zero flag not set
JS ;Jump if sign flag is set
JNS ;Jump if sign flag not set
JP ;Jump if parity flag is set
JNP ;Jump if not parity
JO ;Jump if overflow;
JNO ;Jump if not overflow

## Slide 15: Conditional jumps after signed operand comparison
JG Jump if greater
JNG Jump if not greater
JGE Jump if greater or equal
JNGE Jump if not greater or equal
JL Jump if less
JNL jump if not less
JLE Jump if less or equal
JNLE jump if not less or equal

## Slide 16: Conditional jumps after unsigned operand comparison
JA Jump if above
JNA Jump if not above
JAE Jump if above or equal
JNAE Jump if not above or equal
JB Jump if below
JNB Jump if not below
JBE Jump if below or equal
JNBE jump if not below or equal

## Slide 17: Conditional JMP instructions-Examples
Task: If (N1>N2) copy N1 into DX else copy N2 in DX?
  Start:
  MOV AX, [N1]
  CMP AX, [N2]
  JG L1 ; jump if AX is greater than N2
  MOV DX, N2 ; else statement
  JMP skip
  L1: MOV DX, [N1]
  skip:
  MOV AX,0x4C00
  INT 21H
  N1 DW 5;
  N2 DW 7;

## Slide 18: Signed number comparison-Example?
After executing the following code what value would be placed in AX register?
Note that in signed notation 5 is greater than -1.
  MOV AL, 5
  MOV BL, -1
  CMP AL, BL
  JG L1 ; signed statement; jump if greater …
  MOV AX, 0
  JMP Exit
  L1:
  MOV AX, 1
  Exit:

## Slide 19: Unsigned number comparison-Example?
After executing the following code what value would be placed in AX register?
Note that in unsigned notation 5 is less than -1=FF=255.
  MOV AL, 5
  MOV BL, -1
  CMP AL, BL
  JA L1 ; unsigned statement; jump if above …
  MOV AX, 0
  JMP Exit
  L1:
  MOV AX, 1
  Exit:

## Slide 20: Example? Extended multiplication
Numerical Example
Algorithm
4-bit multiplier;
N1=13 =1101
N2=05 =0101
--------------------
N1*N2? 1101
0000x
1101xx
0000xxx
--------------------
65 = 1000001
again:
Shift right N2 by 1-bit;
If CF is not 1
Shift left N1
Else
Add N1 into the result and then shift left
Repeat from label again until N2 becomes zero.

## Slide 21: Example?
Algorithm
Code
again:
Shift right N2 by 1-bit;
If CF is not 1
Shift left N1
Else
Add N1 into the result and then shift left
Repeat from label again until N2 becomes zero.
MOV AL,N1
MOV BL,N2
MOV CX,4;
L1: SHR BL,1
JNC skip
ADD RESULT,AL;
skip: SHL AL,1
CMP BL,0
JNE L1;
.EXIT
N1 DB 6
N2 DB 5
RESULT DB ?

## Slide 22: Example?
What will be the value of AX register after execution of following code?
  Start:
  MOV AX, 0
  MOV CX, 0x7FF0
  L1:
  ADD AX, 1
  ADD CX, AX
  JNO L1
  END:

## Slide 23: Example?
If (n1+n2) is less than or equal to (n1-n2) then copy (n1+n2) into variable Result; else copy (n1-n2) into variable Result.
start:
; your code ????
.exit
n1 db 44
n2 db 23
result db ?

## Slide 24: Task
Write assembly language program to compare two signed numbers. Numbers are in AX and BL registers. Your program should work as follows:
If AX is greater than BL, then place “0” in AX else place “0” in BL.

## Slide 25: Nested if-else structure ?
Implement following expression in assembly language?
  If (num1==num2 & num1>0 )
  Result=num1+num2;
  ElseIf (num1<num2)
  Result=num1+1;
  End
  Where num1, num2 and Result are word type variables.