## Slide 1: Extended SHIFTING, ADDITION, AND SUBTRACTION
IRFAN.ANJUM@UCP.EDU.PK

## Slide 2: Extended operations
Perform operations on operands greater than the size of underlined architecture’s data bus size?
For example, you want to shift, add or subtract a 64 number when you have 16-bit architecture?
Using extended operation’s technique one can operate on an operand of any size.

## Slide 3: Extended shifting
You want to shift a number left/right greater than the size of your underlined architecture’s data bus size?
Shift left/right a 32-bit or 64-bit number given 16-bit architecture?
You can only shift 16-bits at a time using shift instructions
How to do this?

## Slide 4: Left shift 32-bit number
16-31 bits
CF
0-15 bits
RCL …?
SHL …?
16-31 bits
0-15 bits
0-31 bits
Code:
SHL [NUM1], 1; NUM1=FFFE, CF=1
RCL [NUM1+2],1;
RET
NUM1 DD 0x0000FFFF

## Slide 5: Extended shift operations-exercise
How to shift right a 32-bit number?
How would you shift 64-bit number?

## Slide 6: Extended addition
Suppose you want to add two 32-bit numbers using a 16-bit architecture?
You can add16-bits at a time, how would you do this?
16-31 bits
0-15 bits
16-31 bits
0-15 bits
Num1 dd 0x0001 FFFF
Num2 dd 0x0001 0002
SUM dd 0
16-31 bits
0-15 bits
CF

## Slide 7: Extended addition
Solution:
Add least 16-bits of two numbers, note down if carry is generated (CF=1) ?
Now add upper 16-bits of those two numbers and add the value of CF to upper 16-bits result.
ADC instruction adds value of CF automatically to the result.
ADC AX, BX; AX=AX+BX+CF;

## Slide 8: Extended addition-code
LEA BX, NUM1; load address of first variable. BX points to the lowest byte in Num1.
MOV AX, [BX] loads two bytes into AX register, AX=FFFF
ADD AX, [BX+4]; adds operand at [BX+4] into AX; AX=AX+0002;
MOV [BX+8],AX; save the result in destination double word SUM at lower word which is at offset [BX+8]
MOV AX, [BX+2] load higher word into Ax register, AX=0001
ADC AX, [BX+6]; add higher word of Num2 into AX with carry flag; AX=AX+0001+CF
MOV [BX+10],AX; Write the result into destination double word SUM at upper word which is at offset [BX+10]
.exit
Num1 dd 0x0001 FFFF
Num2 dd 0x0001 0002
SUM dd 0
How would you add two 64-bit numbers?

## Slide 9: Extended subtraction
Suppose you want to subtract two 32-bit numbers using a 16-bit architecture?
You can subtract16-bits at a time, how would you do this?
16-31 bits
0-15 bits
16-31 bits
0-15 bits
Num1 dd 0x0001 FFFF
Num2 dd 0x0001 0002
Diff dd 0
16-31 bits
0-15 bits
CF

## Slide 10: Extended subtraction
Solution:
Subtract least 16-bits of two numbers, note down if borrow is taken (CF=1) ?
Now subtract upper 16-bits of those two numbers and subtract the value of CF (borrow) from upper 16-bits result.
SBB instruction subtracts value of CF (borrow) automatically from the result.
SBB AX, BX; AX=AX-BX-CF;

## Slide 11: Extended subtraction-code
LEA BX, NUM1;
MOV AX, [BX]
SUB AX, [BX+4];
MOV [BX+8],AX;
MOV AX, [BX+2]
SBB AX, [BX+6];
MOV [BX+10],AX;
How would you subtract two 64-bit numbers?

## Slide 12: Exercise?
Suppose ax contains the data which represents the current date, for example
Year, month, day.
Year can vary from 0-99, month can vary from 1-12 and day can vary from 0-31;
Least five bits of AX (0-4) represent value of day, bits (5-8) represent month and bits (9-15) denote the year.
Let’s say the date is year/month/day as 97/06/15, value in AX register would be AX=1100001 0110 01111.
Write program which would identify the day, month and year from AX and place the result in byte type memory variables year, month and day.
Program should work for any date value?