## Slide 1: Arithmetic Logic instructions
IRFAN.ANJUM@UCP.EDU.PK

## Slide 2: Logical instructions
NOT instruction
AND instruction
OR instruction
XOR instruction
Test instruction

## Slide 3: tRuth tabLe
A | B | A | AND | B | A | OR | B | A | XOR | B
0 | 0 |  | 0 |  |  | 0 |  |  | 0 | 
0 | 1 |  | 0 |  |  | 1 |  |  | 1 | 
1 | 0 |  | 0 |  |  | 1 |  |  | 1 | 
1 | 1 |  | 1 |  |  | 1 |  |  | 0 | 
A | NOT | A’
0 | 1 | 
1 | 0 | 

## Slide 4: Syntax
AND destination, source
OR destination, source
XOR destination, source
NOT destination
Destination
  Result is stored in destination
  Can be a Register or Memory Location
Source:
  May be a Constant, Register or Memory Location
Source and destination can not be memory operand in single instruction.

## Slide 5: And INSTRUCTION-example
MOV AL,0xAA
AND AL, 0xF0
1010 0000
1010 1010
1111 0000

## Slide 6: Or INSTRUCTION-EXAMPLE
MOV AL,0xAA
OR AL,0xF0
1010 1010
1111 0000
1111 1010

## Slide 7: Xor INSTRUCTION-exampLe
MOV AL,0xAA
XOR AL, 0xF0
0101 1010
1010 1010
1111 0000

## Slide 8: EffEcts on flags
SF,ZF,PF gets set or reset depending upon the result produced.
AF is undefined
CF,OF = 0

## Slide 9: nOt instruction-EXAMPLE
Performs the one’s complement operation on the destination
MOV AX, 0X00FF; AX=0000 0000 1111 1111
NOT AX; AX=1111 1111 0000 0000
Doesn’t effect any flag.

## Slide 10: MasK operations
To modify only selective bits in destination, we construct a source bit pattern known as MASK
To choose mask, use following properties:
b AND 1 = b (Unchanged)
b AND 0 = 0 (Clear)
b OR 1 = 1 (Set)
b OR 0 = b (Unchanged)
b XOR 0 = b (Unchanged)
b XOR 1 = b’ (Complement)

## Slide 11: MASK operations-clear
–
The AND Instruction:
May be used to clear specific destination bits while preventing the others.
–
–
A 0 mask bit clears the corresponding destination bit.
A 1 mask bit preserves the corresponding destination bit.

## Slide 12: Example
Task: Clear the sign bit of AL while leaving the other bits unchanged?
Solution:
AND AL,7Fh
Where 7Fh (0111 1111) is the mask.

## Slide 13: Mask operations-Set
The OR Instruction:
May be used to SET specific destination bits while preventing the others.
A 1 mask bit sets the corresponding destination bit.
A 0 mask bit preserves the corresponding destination bit.

## Slide 14: ExaMplE:
Set the MSB and LSB of AL while preserving the other bits?
Solution:
OR AL,81h
Where 81h (1000 0001) is the mask.

## Slide 15: Mask operations-complement
The XOR Instruction:
May be used to Complement specific destination bits while preventing the others.
A 1 mask bit complements the corresponding destination bit.
A 0 mask bit preserves the corresponding destination bit.

## Slide 16: ExaMplE
Change the sign bit of DX?
Solution:
XOR DX,8000h
Where 80h ( 1000 0000 ) is the mask.

## Slide 17: Clearing a register-Efficient way to it
;Takes 3 bytes in memory
; Takes 2 bytes
MOV AX,0 OR
SUB AX,AX
OR
XOR AX,AX
; Takes 2 bytes
Choose operation wisely; Above three instructions does the same operation; Initialize register value to ZERO but takes different bytes in memory.

## Slide 18: testing a register FOr ZerO:
CMP CX,0
This instruction is same like :
OR CX,CX
In both instructions, ZF becomes 1 if CX is 0
CMP instruction takes three bytes in memory whereas OR instruction with register operands takes two bytes and destination is also unchanged.

## Slide 19: Check a specific bit status
For example, you want to check the status of 7th bit in a 16-bit register, how to do that?
AND instruction?
AND ax, 0080h;
If 7th bit is zero, zero flag will be set otherwise zero flag will be reset to zero.
Any problem with this instruction?
It changes destination register.

## Slide 20: Test instruction
Test instruction works like AND instruction
With the difference that this instruction only updates flags without changing the destination.
Syntax
  Test destination, source
  Destination can be register/memory
  Source can be register/memory/immediate.

## Slide 21: Test instruction-application
Can be used to check the status of one or more specific bits
For example, if you are required to check the status of 7th bit in a 16-bit register, you can write
Test ax, 0x0080;
ZF will be set if 7th bit in AX is zero. ZF will be zero if 7th bit in AX is 1.
Only ZF is updated keeping ax unchanged.