## Slide 1: Multiply, divide and sign extension
IRFAN.ANJUM@UCP.EDU.PK

## Slide 2: Instructions covered
MUL instruction
Sign extension instructions
  CBW
  CWD
DIV instruction
IMUL instruction
IDIV instruction

## Slide 3: Binary multiplication
We can save time if we replace multiplication with shifting operation even if we need to add afterwards:
AX*36= AX(32+4)= AX*32+ AX*4;
Code:
MOV BX, AX; Make a copy of AX in BX
SHL AX, 5 ;This will multiply number in AX by 32
SHL BX, 2 ; This will multiply number in BX by 4
ADD AX, BX ;Finally add both shifted numbers to get complete result.

## Slide 4: Multiplication and division instructions
Intel’s 8086 architecture allows you to multiply and divide 8-bit or 16-bit operands
Multiplication and division instructions are different for signed and unsigned operands
For unsigned operations instructions are:
  MUL
  DIV
For signed operations instructions are:
  IMUL
  IDIV

## Slide 5: MUL instruction
In MUL instruction only multiplier is specified.
Second operand, the multiplicand, is always AL or AX depending upon the multiplier size.
If multiplier is 8-bits, it will be multiplied with AL
If multiplier is 16-bits, it will be multiplied with AX.
How big the result can be?
Multiplication of two 4-bit unsigned numbers will require destination size to be?
Destination size must be double than the multiplier size.
Notes: Product of two 4-bit numbers will require destination size to be 8-bits. For example if you multiply (1111) with (1111), result would be (225 decimal). It requires 8-bits to fit in.

## Slide 6: MUL instruction-example 8-bit multiplier
MOV AL, 2 ; AL=02
MOV BL, 4 ; BL=04
MUL BL ; AX=AL*BL=0008 in hex format.
Multiplier BL is 8-bits, it gets multiplied with AL and result is stored in AX register.
To confirm that result is stored in AX, use following example:
MOV AL, 64
MOV BL, 4
MUL BL ; AX=AL*BL=0100 hex or 256 in decimal.

## Slide 7: MUL instruction-example 16-bit multiplier
For 16-bit operands, result can be large enough to require 32-bits to specify correctly.
-Example:
MOV AX, 0x0100 ; AX=0100 hex or 256 in decimal
MOV BX, 0x2000 ; BX=2000 hex or 8192 in decimal
MUL BX ; Result=0020 0000 in hex format or 2097152 in decimal. ; 0020 is stored in DX and 0000 is stored in AX.

## Slide 8: MUL instruction- operands
Multiplicand | Multiplier | Destination product
AL | Reg8/mem8 | AX
AX | Reg16/mem16 | DX: AX
EAX | Reg32/mem32 | EDX: EAX

## Slide 9: MUL instructions-flags
The MUL instruction sets the Carry and Overflow flags if the upper half of the product is not equal to zero. – E.g., if AX is multiplied by a 16-bit multiplier, the product is stored in DX:AX. IF the DX is not zero, the Carry and Overflow flags are set.
Rest of the flags change unpredictably.

## Slide 10: CBW,CWD instructions (Sign extension)
How do you process two operands, when one operand is byte sized and second is word sized?
You make them same sized. How?
Append all 0’s to higher byte if number is positive
Append all 1’s to higher byte if number is negative
You can use dedicated instructions to do this automatically
CBW ; Convert byte into word; operates on AL, extends its sign to AH.
CWD ; Convert word into double word; operates on AX, extends its sign to DX.

## Slide 11: CBW; Convert byte to word- examples
MOV AH, 0 ; AH=0000 0000;
MOV AL, 0x80 ; AL=1000 0000; Sign bit of AL is 1, so all 1’s will be copied to AH.
CBW ; AX= ?
AX=1111 1111 1000 0000
MOV AH, 0xFF ; AH=1111 1111
MOV AL, 0x7F ; AL =0111 1111; Sign bit of AL is 0, so all 0’s will be copied to AH.
CBW ; AX= ?
AX=0000 0000 0111 1111

## Slide 12: CWD; Convert word to double word- examples
MOV DX, 0 ; DX=0000 0000 0000 0000;
MOV AX, 0x8000 ; AX=1000 0000 0000 0000; Sign bit of AX is 1;
CWD ; DX: AX= ?
1111 1111 1111 1111 1000 0000 0000 0000
MOV DX, 0xFFFF ; AH=1111 1111 1111 1111
MOV AX, 0x7FFF ; AX=0111 1111 1111 1111; Sign bit of AX is 0, so all 0’s will be copied to DX.
CWD ; DX: AX= ?
0000 0000 0000 0000 0111 1111 1111 1111

## Slide 13: DIV instruction
In DIV instruction only divider is specified.
Second operand, the dividend, is always AX or DX:AX depending upon the size of divider.
If divider is 8-bit operand, dividend is AX.
If divider is 16-bit operand, dividend is combined value of DX and AX such as DX: AX.
A divide operation produces Quotient and Remainder.
For 8-bit divider, Quotient is stored in AL and Remainder is stored in AH.
For 16-bit divider, Quotient is stored in AX and Remainder is stored in DX.

## Slide 14: Div instruction-examples
MOV AL, 9 ;
MOV BL, 4 ;
DIV BL ;Divides AX/BL, gives AL=02 (quotient) and AH=01 (remainder);
In this example, it is assumed that value in AH=0. If value in AH is not zero, same code will produce different results.
MOV AH,01
MOV AL,9 ; AX=0109
MOV BL, 4 ; BL=04
DIV BL ; 265/4 gives quotient AL=42 hex (66 decimal) and remainder AH=01.
So, you have to be careful while dividing. AX must contain only that number which you want to divide.
If dividend is in AL, make sure to sign extend AL to AH before division.

## Slide 15: Division after sign extending AL
MOV AH,01
MOV AL,9 ; AX=0109
CBW ; Sign of AL is copied in all bits of AH. AX= AH: AL= 0009;
MOV BL, 4 ; BL=04
DIV BL ; 0009/4 gives quotient AL=02 and remainder AH=01.
This division gives proper results by dividing 9 with 4.

## Slide 16: Div instruction-examples
MOV DX, 1 ; DX=0001
MOV AX, 6 ; AX=0006
; DX: AX combined becomes (00010006) hex and (65542 in decimal)
MOV BX, 4;
DIV BX ;Divides [DX:AX]/BX, gives AX=4001 (quotient) and DX=02 (remainder);
So, you have to be careful while dividing. DX:AX combined must contain only that number which you want to divide.
If dividend is in AX, make sure to sign extend AX to DX before division.
CWD can be used to sign extend AX to DX before division instruction.

## Slide 17: Division after sign extending AX
MOV DX, 1 ; DX=0001
MOV AX, 6 ; AX=0006
CWD
; This copies sign of AX into all bits of DX. Since sign of AX=0, so DX will become 0. DX:AX combined becomes (0000 0006) hex and (6 in decimal).
MOV BX, 4;
DIV BX ;Divides [DX:AX]/BX, gives AX=0001 (quotient) and DX=02 (remainder);

## Slide 18: IMUL instruction
One main difference in MUL and iMUL instruction is that iMUL is used when operands are treated as signed numbers.
MOV AL, -1 ; AL=FF is (255 in unsigned format)
MOV BL, 2
MUL BL ; Produces AX=01FE hex (510 in decimal); Unsigned product considering ; unsigned operands.
MOV AL, -1 ; AL=FF is (-1 in signed format)
MOV BL, 2
IMUL BL ; Produces AX=FFFE hex (-2 in decimal); Signed product considering ; signed operands.

## Slide 19: Idiv instruction
One main difference in DIV and iDIV instruction is that IDIV is used when operands are treated as signed numbers.
MOV AL, 5 ; AL=05
MOV BL, -2 ; BL=FE (254 in decimal in unsigned notation)
DIV BL ; Produces Quotient AL=00 and Remainder AH=05 considering unsigned operands.
MOV AL, 5 ; AL=05
MOV BL,-2 ; BL=FE (-2 in decimal in signed notation)
IDIV BL ; Produces Quotient AL=FE hex (-2 in decimal) and Remainder AH=01 considering unsigned operands.

## Slide 20: DIV-IDIV instructions- operands
Divider | Quotient | Remainder | Dividedend
Reg8/mem8 | AL | AH | AX
Reg16/mem16 | AX | DX | Combined value of DX:AX
Reg32/mem32 | EAX | EDX | Combined value of EDX:EAX

## Slide 21: Divide overflow-Error
In division operations (DIV and IDIV), when divider is too small as compared with dividend, divide instructions can produce a quotient that might be too large to fit in destination register. For example:
MOV AX, 600
MOV BL,2
DIV BL;
Dividing 600/2 gives quotient=300 which can’t fit in AL register. So divide overflow occurs and program execution is stopped and an error message is displayed.
How to divide in such situations?
Use DIV BX instead of DIV BL.
DIV BX will place quotient in AX which can easily store values up to 65,535.