## Slide 1: Shift, rotate instructions
IRFAN.ANJUM@UCP.EDU.PK

## Slide 2: shift instructions
SHL Instruction (shift left)
SHR Instruction (shift right)
SAL Instruction (shift Arithmetic left)
SAR Instruction (shift Arithmetic right)

## Slide 3: sHl (logical sHiFt leFt)
The SHL (shift left) instruction performs a logical left shift on the destination operand, inserting 0 from LSB position. MSB is shifted to CF.
MOV AL, 2
SHL AL, 1; AL=04; CF=0;
MOV AX, 0xFFFF
SHL AX, 1; AX=FFFE; CF=1;

## Slide 4: sHr (logical rigHt sHiFt)
The SHR (shift right) instruction performs a logical right shift on the destination operand.
Inserts 0 from MSB position. LSB is shifted to CF.
MOV DL, -4; DL=FC
SHR DL,1; DL=7E, CF=0;

## Slide 5: SAL (Shift arithmetic left)
Identical to logical shift left (SHL)
Used for signed operations, when sign of shifted number is important
MOV AL, 2
SAL AL, 1; AL=04; CF=0;
MOV AX, 0xFFFF
SAL AX, 1; AL=FFFE; CF=1;

## Slide 6: sar (Shift arithmetic right)
SAR (shift arithmetic right) performs a right arithmetic shift on the destination operand.
Shifted out bit is copied to CF
MSB remains unchanged and is also copied to next bit position
  MOV AL, -4; AL=FC
  SAR AL, 1; AL=FE; (-2 in decimal)

## Slide 7: Shift operations-syntax
Operation destination, Number_of_shifts
Destination
  Can be a register or memory.
Number_of_Shifts
  Shift can be specified via immediate 8-bit number or CL register.
Operation reg,imm8
Operation mem,imm8
Operation reg,CL
Operation mem,CL

## Slide 8: Problem with Shift instructions?
Shifted out bits in shift operations are lost.
Solution?
  Use ROTATE instructions instead of shift instructions.
In rotate instructions, shifted bits aren’t lost.
Bits ejected from one side are inserted from other side of the same destination.

## Slide 9: Rotate instructions
ROL Instruction (Rotate left )
ROR Instruction (Rotate right)
RCL Instruction (Rotate through Carry left)
RCR Instruction (Rotate through Carry Right)

## Slide 10: ROL Instruction
ROL (rotate left) shifts each bit to the left
The highest bit is copied into both the Carry flag and into the lowest bit
No bits are lost
mov | al,11110000b | 
rol | al,1 | ; AL = 11100001b
mov rol | dl,3Fh dl,2 | ; DL = FC

## Slide 11: ROR Instruction
ROR (rotate right) shifts each bit to the right
The lowest bit is copied into both the Carry flag and into the MSB position
No bits are lost
mov ror | al,11110000b al,1 | ; | AL | = 01111000b
mov ror | dl,3Fh dl,4 | ; | DL | = F3

## Slide 12: RcL Instruction
RCL (rotate carry left) shifts each bit to the left
Copies the Carry flag to the least significant bit
Copies the most significant bit to the Carry flag
CLC |  |  | CLEAR CF |  | CF=0 | 
mov | bl,88h | ; | CF,BL | = | 0 | 10001000b
rcl | bl,1 | ; | CF,BL | = | 1 | 00010000b
rcl | bl,1 | ; | CF,BL | = | 0 | 00100001b

## Slide 13: RcR InstRuctIOn
RCR (rotate carry right) shifts each bit to the right
Copies the Carry flag to the most significant bit
Copies the least significant bit to the Carry flag
STC; SET CARRY, CF=1
MOV AH,10h; AH=0001 0000, CF=1
RCR AH,1; AH=1000 1000, CF=0

## Slide 14: Rotate instructions-syntax
Operation destination, number_of_rotations
Destination can be a memory or a register
Number of rotations can be specified via 8-bit immediate value or via CL register.

## Slide 15: Shift, Rotate instructions- Effect on flag register
Zero flag, Sign flag, Parity flag; each gets set or reset depending upon the result as in add/sub instructions.
Carry flag gets set/reset depending upon the bit that is shifted out of register.
Overflow flag is set whenever sign change occurs in destination operand.
Auxiliary flag is unpredictable.

## Slide 16: applications
1-bit left shift multiplies a number by 2.
1-bit right shift divides a number by 2.
Check if number is even or odd? Right shift and check CF. If CF=0, number is even, otherwise number is odd.
Check if number is positive or negative? Left shift and check CF. If CF=0, number is positive, otherwise number is negative.
Display binary bit patterns by separating bits.
Shifting multiple double words.