## Slide 1: STACK AND SUBROUTINES/PROCEDURES
IRFAN.ANJUM@UCP.EDU.PK

## Slide 2: TOPICS COVERED
Introduction to Stack
Stack operations
  Push operation
  Pop operation
Subroutines/Procedures
  Call instruction
  Ret instruction
  Subroutine-example
  Subroutine-Parameter passing
  Subroutine-Creating local variables

## Slide 3: WHY STACK MEMORY?
Processor needs dedicated memory to perform its operations successfully as Processor has limited number or registers.
Operations?
  Processor saves return addresses onto stack before going to execute a function or interrupt service routine.
  When parameters are to be passed to functions, they are passed through the stack.
  Local variables created within functions are stored temporarily onto stack.
Stack is managed directly by the CPU using stack pointer (SP)
Stack pointer (SP) is a CPU register which points to the stack memory address from where data is to be accessed.

## Slide 4: ACCESSING STACK MEMORY
Stack is also accessible to the programmer for data write/read operations.
To write a value into stack memory, one can write PUSH source; where source is the value to be written into stack. Example:
PUSH AX ; Saves value of AX onto stack.
Similarly, to delete a value from stack, one can write Pop destination; This instruction removes value from stack and saves it into destination. Example:
Pop AX ; Removes value from stack and places it into AX.

## Slide 5: Using Push and Pop instructions-Example
What will be value of AX and n2 after execution of following code? Start: MOV AX, 0xAB12; Push AX; ; AB12 saved on stack; Push n2; ; FFEE saved on stack; Pop AX; ; Top of stack is moved to AX, so AX=FFEE; Pop n2; ; Next value in stack is moved to num2, so n2=AB12 ret n2 dw 0xFFEE;
Swapped two numbers without third variable?

## Slide 6: Push source
Stack pointer (SP) contains an address that tells processor where to write data whenever a push instruction is executed.
A push instruction (PUSH source) does following operations
SP=SP-2
M[SP]=source
For example if SP=FFFE and AX is 12AB; when Push AX is executed, SP is decremented to FFFC and value 12AB is saved on memory address FFFC.
After execution, SP becomes FFFC.
Note that source value (AX in this case) doesn’t change in push operation.

## Slide 7: Stack memory window
Memory addresses | Values in STACK
0000 | 
0002 | 
0004 | 
… | 
… | 
FFF6 | 
FFF8 | 
FFFA | 
FFFC | 
FFEE | ----
Initially SP points to the address

## Slide 8: Push instruction and its effect
Memory addresses | Values in STACK
0000 | 
0002 | 
0004 | 
… | 
… | 
FFF6 | 
FFF8 | 
FFFA | 
FFFC | Value of AX
FFEE | ----
Initially SP points to the address
When you write, push AX?
SP is decremented by 2 and value is stored at specified address.
SP=SP-2; SP=FFFC
MEM[SP]=AX
Now SP points to the address

## Slide 9: Push instruction and its effect
Memory addresses | Values in STACK
0000 | 
0002 | 
0004 | 
… | 
… | 
FFF6 | 
FFF8 | 
FFFA | 
FFFC | Value of AX
FFEE | Garbage value
Initially SP points to the address
SP always points to last pushed value on stack. Currently pointing to value of AX, located at address FFFC
Now SP points to the address

## Slide 10: Accessing data randomly from stack
Memory addresses | Values in STACK
0000 | 
0002 | 
0004 | 
… | 
… | 
FFF6 | 
FFF8 | 000C
FFFA | 0007
FFFC | 0005
FFEE | Garbage value
Initially SP points to the address
Now SP points to the address
MOV AX, 5
MOV BX, 7
PUSH AX
PUSH BX
ADD AX, BX
PUSH AX; Did 5+7 and saved on stack
Now I want to do 5-7?
AX is changed, read its value from stack?

## Slide 11: Accessing data randomly from stack
Memory addresses | Values in STACK
0000 | 
0002 | 
0004 | 
… | 
… | 
FFF6 | 
FFF8 | 000C
FFFA | 0007
FFFC | 0005
FFEE | Garbage value
Initially SP points to the address
MOV AX, 5
MOV BX, 7
PUSH AX
PUSH BX
ADD AX, BX
PUSH AX; Did 5+7 and saved on stack
MOV BP, SP
MOV AX, [BP+4]; AX=5
Now SP & BP points to the same address

## Slide 12: Subroutine/Functions
JMP START
; variable declaration
; function declaration
; main program
START:
; function calling
.EXIT

## Slide 13: Function to calculate factorial of a number?
JMP START
Num1 dw 5; variables needed in function
Fact dw ?
MyFunction
……. function statements
ret
START:
Call MyFunction; function calling
.EXIT